Skeinforge settings documentation

The idea for this documentation is that all the settings in the skeinforge application are commented because somtimes it is hard to know what they are good for.
Everybody is free to change something and upload it again to the reprap forums

# Bottom

This page is in the table of contents.
Bottom sets the bottom of the carving to the defined altitude.

==Operation==
The default 'Activate Bottom' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Additional Height over Layer Thickness===
Default is half.

The layers will start at the altitude plus the Additional Height over Layer Thickness times the layer thickness. The default value of half means that the bottom layer is at the height of the bottom slice, because each slice is made through the middle of each layer. Raft expects the layers to start at an additional half layer thickness. You should only change Additional Height over Layer Thickness if you are manipulating the skeinforge output with your own program which does not use the raft tool.

===Altitude===
Default is zero.

Defines the altitude of the bottom of the model. The bottom slice have a z of the altitude plus half the layer thickness.

===SVG Viewer===
Default is webbrowser.

If the 'SVG Viewer' is set to the default 'webbrowser', the scalable vector graphics file will be sent to the default browser to be opened. If the 'SVG Viewer' is set to a program name, the scalable vector graphics file will be sent to that program to be opened.

==Examples==
The following examples bottom the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and bottom.py.

> python bottom.py
This brings up the bottom dialog.

> python bottom.py Screw Holder Bottom.stl
The bottom tool is parsing the file:
Screw Holder Bottom.stl
..
The bottom tool has created the file:
.. Screw Holder Bottom_bottom.gcode

# Carve

This page is in the table of contents.
Carve is a script to carve a shape into svg slice layers.

The carve manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Carve

On the Arcol Blog a method of deriving the layer thickness is posted. That article "Machine Calibrating" is at:
http://blog.arcol.hu/?p=157

==Settings==
===Add Layer Template to SVG===
Default is on.

When selected, the layer template will be added to the svg output, which adds javascript control boxes. So 'Add Layer Template to SVG' should be selected when the svg will be viewed in a browser.

When off, no controls will be added, the svg output will only include the fabrication paths. So 'Add Layer Template to SVG' should be deselected when the svg will be used by other software, like Inkscape.

===Extra Decimal Places===
Default is two.

Defines the number of extra decimal places export will output compared to the number of decimal places in the layer thickness. The higher the 'Extra Decimal Places', the more significant figures the output numbers will have.

===Import Coarseness===
Default is one.

When a triangle mesh has holes in it, the triangle mesh slicer switches over to a slow algorithm that spans gaps in the mesh. The higher the 'Import Coarseness' setting, the wider the gaps in the mesh it will span. An import coarseness of one means it will span gaps of the perimeter width.

===Infill in Direction of Bridge===
Default is on.

When selected, the infill will be in the direction of any bridge across a gap, so that the fill will be able to span a bridge easier.

===Layer Thickness===
Default is 0.4 mm.

Defines the thickness of the extrusion layer at default extruder speed, this is the most important carve setting.

===Layers===
Carve slices from bottom to top. To get a single layer, set the "Layers From" to zero and the "Layers To" to one. The 'Layers From' until 'Layers To' range is a python slice.

====Layers From====
Default is zero.

Defines the index of the bottom layer that will be carved. If the 'Layers From' is the default zero, the carving will start from the lowest layer. If the 'Layers From' index is negative, then the carving will start from the 'Layers From' index below the top layer.

====Layers To====
Default is a huge number, which will be limited to the highest index layer.

Defines the index of the top layer that will be carved. If the 'Layers To' index is a huge number like the default, the carving will go to the top of the model. If the 'Layers To' index is negative, then the carving will go to the 'Layers To' index below the top layer.

===Mesh Type===
Default is 'Correct Mesh'.

====Correct Mesh====
When selected, the mesh will be accurately carved, and if a hole is found, carve will switch over to the algorithm that spans gaps.

====Unproven Mesh====
When selected, carve will use the gap spanning algorithm from the start. The problem with the gap spanning algothm is that it will span gaps, even if there is not actually a gap in the model.

===Perimeter Width over Thickness===
Default is 1.8.

Defines the ratio of the extrusion perimeter width to the layer thickness. The higher the value the more the perimeter will be inset, the default is 1.8. A ratio of one means the extrusion is a circle, a typical ratio of 1.8 means the extrusion is a wide oval. These values should be measured from a test extrusion line.

===SVG Viewer===
Default is webbrowser.

If the 'SVG Viewer' is set to the default 'webbrowser', the scalable vector graphics file will be sent to the default browser to be opened. If the 'SVG Viewer' is set to a program name, the scalable vector graphics file will be sent to that program to be opened.

==Examples==
The following examples carve the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and carve.py.

> python carve.py
This brings up the carve dialog.

> python carve.py Screw Holder Bottom.stl
The carve tool is parsing the file:
Screw Holder Bottom.stl
..
The carve tool has created the file:
.. Screw Holder Bottom_carve.svg

# Chamber

This page is in the table of contents.
Some filaments contract too much and to prevent this you have to print the object in a temperature regulated chamber or on a temperature regulated bed. The chamber tool allows you to control the bed and chamber temperature and the holding pressure. The gcodes are also described at:
http://reprap.org/wiki/Mendel_User_Manual:_RepRapGCodes

The chamber manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Chamber

==Operation==
The default 'Activate Chamber' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Bed Temperature===
Default is 60C.

Defines the print_bed temperature in Celcius by adding an M140 command.

===Chamber Temperature===
Default is 30C.

Defines the chamber temperature in Celcius by adding an M141 command.

===Holding Force===
Default is zero.

Defines the holding pressure of a mechanism, like a vacuum table or electromagnet, to hold the bed surface or object, by adding an M142 command. The holding pressure is in bar. For hardware which only has on/off holding, when the holding pressure is zero, turn off holding, when the holding pressure is greater than zero, turn on holding.

==Heated Beds==
===Bothacker===
A resistor heated aluminum plate by Bothacker:
http://bothacker.com

with an article at:
http://bothacker.com/2009/12/18/heated-build-platform/

===Domingo===
A heated copper build plate by Domingo:
http://casainho-emcrepstrap.blogspot.com/

with articles at:
http://casainho-emcrepstrap.blogspot.com/2010/01/first-time-with-pla-testing-it-also-on.html
http://casainho-emcrepstrap.blogspot.com/2010/01/call-for-helpideas-to-develop-heated.html
http://casainho-emcrepstrap.blogspot.com/2010/01/new-heated-build-platform.html
http://casainho-emcrepstrap.blogspot.com/2010/01/no-acrylic-and-instead-kapton-tape-on.html
http://casainho-emcrepstrap.blogspot.com/2010/01/problems-with-heated-build-platform-and.html
http://casainho-emcrepstrap.blogspot.com/2010/01/perfect-build-platform.html
http://casainho-emcrepstrap.blogspot.com/2009/12/almost-no-warp.html
http://casainho-emcrepstrap.blogspot.com/2009/12/heated-base-plate.html

===Jmil===
A heated build stage by jmil, over at:
http://www.hive76.org

with articles at:
http://www.hive76.org/handling-hot-build-surfaces
http://www.hive76.org/heated-build-stage-success

===Kulitorum===
Kulitorum has made a heated bed. It is a 5mm Alu sheet with a pattern laid out in kapton tape. The wire is a 0.6mm2 Konstantin wire and it's held in place by small pieces of kapton tape. The description and picture is at:
http://gallery.kulitorum.com/main.php?g2_itemId=283

===Metalab===
A heated base by the Metalab folks:
http://reprap.soup.io

with information at:
http://reprap.soup.io/?search=heated%20base

===Nophead===
A resistor heated aluminum bed by Nophead:
http://hydraraptor.blogspot.com

with articles at:
http://hydraraptor.blogspot.com/2010/01/will-it-stick.html
http://hydraraptor.blogspot.com/2010/01/hot-metal-and-serendipity.html
http://hydraraptor.blogspot.com/2010/01/new-year-new-plastic.html
http://hydraraptor.blogspot.com/2010/01/hot-bed.html

===Prusajr===
A resistive wire heated plexiglass plate by prusajr:
http://prusadjs.cz/

with articles at:
http://prusadjs.cz/2010/01/heated-reprap-print-bed-mk2/
http://prusadjs.cz/2009/11/look-ma-no-warping-heated-reprap-print-bed/

===Pumpernickel2===
A resistor heated aluminum plate by Pumpernickel2:
http://dev.forums.reprap.org/profile.php?14,844

with a picture at:
http://dev.forums.reprap.org/file.php?14,file=1228,filename=heatedplate.jpg

===Zaggo===
A resistor heated aluminum plate by Zaggo at Pleasant Software:
http://pleasantsoftware.com/developer/3d/

with articles at:
ttp://pleasantsoftware.com/developer/3d/2009/12/05/raftless/
http://pleasantsoftware.com/developer/3d/2009/11/15/living-in-times-of-warp-free-printing/
http://pleasantsoftware.com/developer/3d/2009/11/12/canned-heat/

==Examples==
The following examples chamber the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and chamber.py.

> python chamber.py
This brings up the chamber dialog.

> python chamber.py Screw Holder Bottom.stl
The chamber tool is parsing the file:
Screw Holder Bottom.stl
..
The chamber tool has created the file:
Screw Holder Bottom_chamber.gcode

# Clip

This page is in the table of contents.
Clip clips the ends of loops to prevent bumps from forming.

The clip manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Clip

==Operation==
The default 'Activate Clip' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Clip Over Perimeter Width===
Default is 0.2.

Defines the ratio of the amount each end of the loop is clipped over the perimeter width. The total gap will therefore be twice the clip. If the ratio is too high loops will have a gap, if the ratio is too low there will be a bulge at the loop ends.

===Maximum Connection Distance Over Perimeter Width===
Default is ten.

Defines the ratio of the maximum connection distance between loops over the perimeter width. If the ratio is zero, nothing will be done. If it is ratio greater than zero, clip will connect nearby loops, combining them into a spiral. For loop connection, nearby means that the distance between a pair of loops is smaller or equal to the maximum connection distance.

==Examples==
The following examples clip the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and clip.py.

> python clip.py
This brings up the clip dialog.

> python clip.py Screw Holder Bottom.stl
The clip tool is parsing the file:
Screw Holder Bottom.stl
..
The clip tool has created the file:
.. Screw Holder Bottom_clip.gcode

# Comb

This page is in the table of contents.
Comb is a script to comb the extrusion hair of a gcode file.

The comb manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Comb

Comb bends the extruder travel paths around holes in the slices, to avoid stringers. It moves the extruder to the inside of perimeters before turning the extruder on so any start up ooze will be inside the shape.

==Operation==
The default 'Activate Comb' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Running Jump Space===
Placeholder.

==Examples==
The following examples comb the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and comb.py.

> python comb.py
This brings up the comb dialog.

> python comb.py Screw Holder Bottom.stl
The comb tool is parsing the file:
Screw Holder Bottom.stl
..
The comb tool has created the file:
.. Screw Holder Bottom_comb.gcode

# Cool

This page is in the table of contents.
Cool is a script to cool the shape.

Cool works well with a stepper extruder, it does not work well with a DC motor extruder.

The cool manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Cool

Allan Ecker aka The Masked Retriever's has written the "Skeinforge Quicktip: Cool" at:
http://blog.thingiverse.com/2009/07/28/skeinforge-quicktip-cool/

==Operation==
The default 'Activate Cool' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Bridge Cool===
Default is one degree Celcius.

If the layer is a bridge layer, then cool will lower the temperature by 'Bridge Cool' degrees Celcius.

===Cool Type===
Default is 'Slow Down'.

====Orbit====
When selected, cool will add orbits with the extruder off to give the layer time to cool, so that the next layer is not extruded on a molten base. The orbits will be around the largest island on that layer. Orbit should only be chosen if you can not upgrade to a stepper extruder.

====Slow Down====
When selected, cool will slow down the extruder so that it will take the minimum layer time to extrude the layer. DC motors do not operate properly at very slow flow rates, so if you have a DC motor extruder, you should upgrade to a stepper extruder, but if you can't do that, you can try using the 'Orbit' option.

===Maximum Cool===
Default is 2 degrees Celcius.

If it takes less time to extrude the layer than the minimum layer time, then cool will lower the temperature by the 'Maximum Cool' setting times the layer time over the minimum layer time.

===Minimum Layer Time===
Default is 60 seconds.

Defines the minimum amount of time the extruder will spend on a layer, this is an important setting.

===Minimum Orbital Radius===
Default is 10 millimeters.

When the orbit cool type is selected, if the area of the largest island is as large as the square of the "Minimum Orbital Radius" then the orbits will be just within the island. If the island is smaller, then the orbits will be in a square of the "Minimum Orbital Radius" around the center of the island.

===Name of Alteration Files===
Cool looks for alteration files in the alterations folder in the .skeinforge folder in the home directory. Cool does not care if the text file names are capitalized, but some file systems do not handle file name cases properly, so to be on the safe side you should give them lower case names. If it doesn't find the file it then looks in the alterations folder in the skeinforge_plugins folder. The cool start and end text idea is from:
http://makerhahn.blogspot.com/2008/10/yay-minimug.html

====Name of Cool End File====
Default is cool_end.gcode.

If there is a file with the name of the "Name of Cool End File" setting, it will be added to the start of the orbits.

====Name of Cool Start File====
Default is cool_start.gcode.

If there is a file with the name of the "Name of Cool Start File" setting, it will be added to the end of the orbits.

===Turn Fan On at Beginning===
Default is on.

When selected, cool will turn the fan on at the beginning of the fabrication.

===Turn Fan On at Ending===
Default is on.

When selected, cool will turn the fan off at the ending of the fabrication.

==Examples==
The following examples cool the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and cool.py.

> python cool.py
This brings up the cool dialog.

> python cool.py Screw Holder Bottom.stl
The cool tool is parsing the file:
Screw Holder Bottom.stl
..
The cool tool has created the file:
.. Screw Holder Bottom_cool.gcode

# Dimensions

This page is in the table of contents.
Dimension adds Adrian's extruder distance E value to the gcode movement lines, as described at:
http://blog.reprap.org/2009/05/4d-printing.html

and in Erik de Bruijn's conversion script page at:
http://objects.reprap.org/wiki/3D-to-5D-Gcode.php

The dimension manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Dimension

Nophead wrote an excellent article on how to set the filament parameters:
http://hydraraptor.blogspot.com/2011/03/spot-on-flow-rate.html

==Operation==
The default 'Activate Dimension' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Extrusion Distance Format Choice===
Default is 'Absolute Extrusion Distance' because in Adrian's description the distance is absolute. In future, because the relative distances are smaller than the cumulative absolute distances, hopefully the firmaware will be able to use relative distance.

====Absolute Extrusion Distance====
When selected, the extrusion distance output will be the total extrusion distance to that gcode line.

====Relative Extrusion Distance====
When selected, the extrusion distance output will be the extrusion distance from the last gcode line.

===Extruder Retraction Speed===
Default is 13.3 mm/s.

Defines the extruder retraction feed rate.

===Filament===
====Filament Diameter====
Default is 2.8 millimeters.

Defines the filament diameter.

====Filament Packing Density====
Default is 0.85. This is for ABS.

Defines the effective filament packing density.

The default value is so low for ABS because ABS is relatively soft and with a pinch wheel extruder the teeth of the pinch dig in farther, so it sees a smaller effective diameter. With a hard plastic like PLA the teeth of the pinch wheel don't dig in as far, so it sees a larger effective diameter, so feeds faster, so for PLA the value should be around 0.97. This is with Wade's hobbed bolt. The effect is less significant with larger pinch wheels.

Overall, you'll have to find the optimal filament packing density by experiment.

===Retraction Distance===
Default is zero.

Defines the retraction distance when the thread ends.

===Restart Extra Distance===
Default is zero.

Defines the restart extra distance when the thread restarts. The restart distance will be the retraction distance plus the restart extra distance.

==Examples==
The following examples dimension the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and dimension.py.

> python dimension.py
This brings up the dimension dialog.

> python dimension.py Screw Holder Bottom.stl
The dimension tool is parsing the file:
Screw Holder Bottom.stl
..
The dimension tool has created the file:
.. Screw Holder Bottom_dimension.gcode

# Export

This page is in the table of contents.
Export is a script to pick an export plugin and optionally print the output to a file.

The export manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Export

==Operation==
The default 'Activate Export' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Also Send Output To===
Default is empty.

Defines the output name for sending to a file or pipe. A common choice is sys.stdout to print the output in the shell screen. Another common choice is sys.stderr. With the empty default, nothing will be done. If the value is anything else, the output will be written to that file name.

===Comment Choice===
Default is 'Delete All Comments'.

====Do Not Delete Comments====
When selected, export will not delete comments. Crafting comments slow down the processing in many firmware types, which leads to segment pauses.

====Delete Crafting Comments====
When selected, export will delete the time consuming crafting comments, but leave the initialization comments. Since the crafting comments are deleted, there are no additional segment pauses. The remaining initialization comments provide some useful information for the analyze tools.

====Delete All Comments====
When selected, export will delete all comments. The comments are not necessary to run a fabricator.

===Export Operations===
Export presents the user with a choice of the export plugins in the export_plugins folder. The chosen plugin will then modify the gcode or translate it into another format. There is also the "Do Not Change Output" choice, which will not change the output. An export plugin is a script in the export_plugins folder which has the getOutput function, the globalIsReplaceable variable and if it's output is not replaceable, the writeOutput function.

===File Extension===
Default is gcode.

Defines the file extension added to the name of the output file.

===Name of Replace File===
Default is replace.csv.

When export is exporting the code, if there is a tab separated file with the name of the "Name of Replace File" setting, it will replace the string in the first column by its replacement in the second column. If there is nothing in the second column, the first column string will be deleted, if this leads to an empty line, the line will be deleted. If there are replacement columns after the second, they will be added as extra lines of text. There is an example file replace_example.csv to demonstrate the tab separated format, which can be edited in a text editor or a spreadsheet.

Export looks for the alteration file in the alterations folder in the .skeinforge folder in the home directory. Export does not care if the text file names are capitalized, but some file systems do not handle file name cases properly, so to be on the safe side you should give them lower case names. If it doesn't find the file it then looks in the alterations folder in the skeinforge_plugins folder.

===Save Penultimate Gcode===
Default is off.

When selected, export will save the gcode file with the suffix '_penultimate.gcode' just before it is exported. This is useful because the code after it is exported could be in a form which the viewers can not display well.

==Examples==
The following examples export the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and export.py.

> python export.py
This brings up the export dialog.

> python export.py Screw Holder Bottom.stl
The export tool is parsing the file:
Screw Holder Bottom.stl
..
The export tool has created the file:
.. Screw Holder Bottom_export.gcode

# Fill

This page is in the table of contents.
Fill is a script to fill the perimeters of a gcode file.

The fill manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Fill

Allan Ecker aka The Masked Retriever has written the "Skeinforge Quicktip: Fill" at:
http://blog.thingiverse.com/2009/07/21/mysteries-of-skeinforge-fill/

==Operation==
The default 'Activate Fill' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Diaphragm===
The diaphragm is a solid group of layers, at regular intervals. It can be used with a sparse infill to give the object watertight, horizontal compartments and/or a higher shear strength.

====Diaphragm Period====
Default is one hundred.

Defines the number of layers between diaphrams.

====Diaphragm Thickness====
Default is zero, because the diaphragm feature is rarely used.

Defines the number of layers the diaphram is composed of.

===Extra Shells===
The shells interior perimeter loops. Adding extra shells makes the object stronger & heavier.

====Extra Shells on Alternating Solid Layers====
Default is two.

Defines the number of extra shells, on the alternating solid layers.

====Extra Shells on Base====
Default is one.

Defines the number of extra shells on the bottom, base layer and every even solid layer after that. Setting this to a different value than the "Extra Shells on Alternating Solid Layers" means the infill pattern will alternate, creating a strong interleaved bond even if the perimeter loop shrinks.

====Extra Shells on Sparse Layer====
Default is one.

Defines the number of extra shells on the sparse layers. The solid layers are those at the top & bottom, and wherever the object has a plateau or overhang, the sparse layers are the layers in between.

===Grid===
====Grid Circle Separation over Perimeter Width====
Default is 0.2.

Defines the ratio of the amount the grid circle is inset over the perimeter width, the default is zero. With a value of zero the circles will touch, with a value of one two threads could be fitted between the circles.

====Grid Extra Overlap====
Default is 0.1.

Defines the amount of extra overlap added when extruding the grid to compensate for the fact that when the first thread going through a grid point is extruded, since there is nothing there yet for it to connect to it will shrink extra.

====Grid Junction Separation over Octogon Radius At End====
Default is zero.

Defines the ratio of the amount the grid square is increased in each direction over the extrusion width at the end. With a value of one or so the grid pattern will have large squares to go with the octogons.

====Grid Junction Separation over Octogon Radius At Middle====
Default is zero.

Defines the increase at the middle. If this value is different than the value at the end, the grid would have an accordion pattern, which would give it a higher shear strength.

====Grid Junction Separation Band Height====
Default is ten.

Defines the height of the bands of the accordion pattern.

===Infill===
====Infill Pattern====
Default is 'Line', since it is quicker to generate and does not add extra movements for the extruder. The grid pattern has extra diagonal lines, so when choosing a grid option, set the infill solidity to 0.2 or less so that there is not too much plastic and the grid generation time, which increases with the third power of solidity, will be reasonable.

=====Grid Circular=====
When selected, the infill will be a grid of separated circles. Because the circles are separated, the pattern is weak, it only provides support for the top layer threads and some strength in the z direction. The flip side is that this infill does not warp the object, the object will get warped only by the walls.

Because this pattern turns the extruder on and off often, it is best to use a stepper motor extruder.

=====Grid Hexagonal=====
When selected, the infill will be a hexagonal grid. Because the grid is made with threads rather than with molding or milling, only a partial hexagon is possible, so the rectangular grid pattern is stronger.

=====Grid Rectangular=====
When selected, the infill will be a funky octogon square honeycomb like pattern which gives the object extra strength.

=====Line=====
When selected, the infill will be made up of lines.

====Infill Begin Rotation====
Default is forty five degrees, giving a diagonal infill.

Defines the amount the infill direction of the base and every second layer thereafter is rotated.

====Infill Odd Layer Extra Rotation====
Default is ninety degrees, making the odd layer infill perpendicular to the base layer.

Defines the extra amount the infill direction of the odd layers is rotated compared to the base layer.

====Infill Begin Rotation Repeat====
Default is one, giving alternating cross hatching.

Defines the number of layers that the infill begin rotation will repeat. With a value higher than one, the infill will go in one direction more often, giving the object more strength in one direction and less in the other, this is useful for beams and cantilevers.

====Infill Perimeter Overlap====
Default is 0.15.

Defines the amount the infill overlaps the perimeter over the average of the perimeter and infill width. The higher the value the more the infill will overlap the perimeter, and the thicker join between the infill and the perimeter. If the value is too high, the join will be so thick that the nozzle will run plow through the join below making a mess, also when it is above 0.45 fill may not be able to create infill correctly. If you want to stretch the infill a lot, set 'Path Stretch over Perimeter Width' in stretch to a high value.

====Infill Solidity====
Default is 0.2.

Defines the solidity of the infill, this is the most important setting in fill. A value of one means the infill lines will be right beside each other, resulting in a solid, strong, heavy shape which takes a long time to extrude. A low value means the infill will be sparse, the interior will be mosty empty space, the object will be weak, light and quick to build.

====Infill Width over Thickness====
Default is 1.5.

Defines the ratio of the infill width over the layer thickness. The higher the value the wider apart the infill will be and therefore the sparser the infill will be.

===Solid Surface Thickness===
Default is three.

Defines the number of solid layers that are at the bottom, top, plateaus and overhang. With a value of zero, the entire object will be composed of a sparse infill, and water could flow right through it. With a value of one, water will leak slowly through the surface and with a value of three, the object could be watertight. The higher the solid surface thickness, the stronger and heavier the object will be.

===Start From Choice===
Default is 'Lower Left'.

Defines where each layer starts from.

====Lower Left====
When selected the layer will start from the lower left corner. This is to extrude in round robin fashion so that the first extrusion will be deposited on the coolest part of the last layer. The reason for this is described at:
http://hydraraptor.blogspot.com/2010/12/round-robin.html

====Nearest====
When selected the layer will start from the nearest point to the end of the last layer. This leads to less stringing, but the first extrusion will be deposited on the hottest part of the last layer which leads to melting problems. So this option is deprecated, eventually this option will be removed and the layers will always start from the lower left.

===Thread Sequence Choice===
The 'Thread Sequence Choice' is the sequence in which the threads will be extruded on the second and higher layers. There are three kinds of thread, the perimeter threads on the outside of the object, the loop threads aka inner shell threads, and the interior infill threads. The first layer thread sequence is 'Perimeter > Loops > Infill'.

The default choice is 'Perimeter > Loops > Infill', which the default stretch parameters are based on. If you change from the default sequence choice setting of perimeter, then loops, then infill, the optimal stretch thread parameters would also be different. In general, if the infill is extruded first, the infill would have to be stretched more so that even after the filament shrinkage, it would still be long enough to connect to the loop or perimeter. The six sequence combinations follow below.

====Infill > Loops > Perimeter====
====Infill > Perimeter > Loops====
====Loops > Infill > Perimeter====
====Loops > Perimeter > Infill====
====Perimeter > Infill > Loops====
====Perimeter > Loops > Infill====

==Examples==
The following examples fill the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and fill.py.

> python fill.py
This brings up the fill dialog.

> python fill.py Screw Holder Bottom.stl
The fill tool is parsing the file:
Screw Holder Bottom.stl
..
The fill tool has created the file:
.. Screw Holder Bottom_fill.gcode

# Fillet

This page is in the table of contents.
Fillet rounds the corners slightly in a variety of ways. This is to reduce corner blobbing and sudden extruder acceleration.

The fillet manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Fillet

==Operation==
The default 'Activate Fillet' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Fillet Procedure Choice===
Default is 'Bevel''.

====Arc Point====
When selected, the corners will be filleted with an arc using the gcode point form.

====Arc Radius====
When selected, the corners will be filleted with an arc using the gcode radius form.

====Arc Segment====
When selected, the corners will be filleted with an arc composed of several segments.

====Bevel====
When selected, the corners will be beveled.

===Corner Feed Rate over Operating Feed Rate===
Default is one.

Defines the ratio of the feed rate in corners over the operating feed rate. With a high value the extruder will move quickly in corners, accelerating quickly and leaving a thin extrusion. With a low value, the extruder will move slowly in corners, accelerating gently and leaving a thick extrusion.

===Fillet Radius over Perimeter Width===
Default is 0.35.

Defines the width of the fillet.

===Reversal Slowdown over Perimeter Width===
Default is 0.5.

Defines how far before a path reversal the extruder will slow down. Some tools, like nozzle wipe, double back the path of the extruder and this option will add a slowdown point in that path so there won't be a sudden jerk at the end of the path. If the value is less than 0.1 a slowdown will not be added.

===Use Intermediate Feed Rate in Corners===
Default is on.

When selected, the feed rate entering the corner will be the average of the old feed rate and the new feed rate.

==Examples==
The following examples fillet the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and fillet.py.

> python fillet.py
This brings up the fillet dialog.

> python fillet.py Screw Holder Bottom.stl
The fillet tool is parsing the file:
Screw Holder Bottom.stl
..
The fillet tool has created the file:
.. Screw Holder Bottom_fillet.gcode

# Home

This page is in the table of contents.
Home is a script to home the tool.

The home manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Home

==Operation==
The default 'Activate Home' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Name of Homing File===
Default is homing.gcode.

At the beginning of a each layer, home will add the commands of a gcode script with the name of the "Name of Homing File" setting, if one exists. Home does not care if the text file names are capitalized, but some file systems do not handle file name cases properly, so to be on the safe side you should give them lower case names. Home looks for those files in the alterations folder in the .skeinforge folder in the home directory. If it doesn't find the file it then looks in the alterations folder in the skeinforge_plugins folder.

==Examples==
The following examples home the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and home.py.

> python home.py
This brings up the home dialog.

> python home.py Screw Holder Bottom.stl
The home tool is parsing the file:
Screw Holder Bottom.stl
..
The home tool has created the file:
.. Screw Holder Bottom_home.gcode

# Hop

This page is in the table of contents.
Hop is a script to raise the extruder when it is not extruding.

The hop manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Hop

==Operation==
The default 'Activate Hop' checkbox is off. It is off because Vik and Nophead found better results without hopping. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Hop Over Layer Thickness===
Default is one.

Defines the ratio of the hop height over the layer thickness, this is the most important hop setting.

===Minimum Hop Angle===
Default is 20 degrees.

Defines the minimum angle that the path of the extruder will be raised. An angle of ninety means that the extruder will go straight up as soon as it is not extruding and a low angle means the extruder path will gradually rise to the hop height.

==Examples==
The following examples hop the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and hop.py.

> python hop.py
This brings up the hop dialog.

> python hop.py Screw Holder Bottom.stl
The hop tool is parsing the file:
Screw Holder Bottom.stl
..
The hop tool has created the file:
.. Screw Holder Bottom_hop.gcode

# Inset

This page is in the table of contents.
Inset will inset the outside outlines by half the perimeter width, and outset the inside outlines by the same amount.

The inset manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Inset

==Settings==
===Add Custom Code for Temperature Reading===
Default is on.

When selected, the M105 custom code for temperature reading will be added at the beginning of the file.

===Bridge Width Multiplier===
Default is one.

Defines the ratio of the extrusion width of a bridge layer over the extrusion width of the typical non bridge layers.

===Loop Order Choice===
Default loop order choice is 'Ascending Area'.

When overlap is to be removed, for each loop, the overlap is checked against the list of loops already extruded. If the latest loop overlaps an already extruded loop, the overlap is removed from the latest loop. The loops are ordered according to their areas.

====Ascending Area====
When selected, the loops will be ordered in ascending area. With thin walled parts, if overlap is being removed the outside of the container will not be extruded. Holes will be the correct size.

====Descending Area====
When selected, the loops will be ordered in descending area. With thin walled parts, if overlap is being removed the inside of the container will not be extruded. Holes will be missing the interior wall so they will be slightly wider than model size.

===Overlap Removal Width over Perimeter Width===
Default is 0.6.

Defines the ratio of the overlap removal width over the perimeter width. Any part of the extrusion that comes within the overlap removal width of another is removed. This is to prevent the extruder from depositing two extrusions right beside each other. If the 'Overlap Removal Width over Perimeter Width' is less than 0.2, the overlap will not be removed.

===Turn Extruder Heater Off at Shut Down===
Default is on.

When selected, the M104 S0 gcode line will be added to the end of the file to turn the extruder heater off by setting the extruder heater temperature to 0.

==Examples==
The following examples inset the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and inset.py.

> python inset.py
This brings up the inset dialog.

> python inset.py Screw Holder Bottom.stl
The inset tool is parsing the file:
Screw Holder Bottom.stl
..
The inset tool has created the file:
.. Screw Holder Bottom_inset.gcode

# Jitter

This page is in the table of contents.
Jitter jitters the loop end position to a different place on each layer to prevent the a ridge from forming.

The jitter manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Jitter

==Operation==
The default 'Activate Jitter' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Jitter Over Perimeter Width===
Default is two.

Defines the amount the loop ends will be jittered over the perimeter width. A high value means the loops will start all over the place and a low value means loops will start at roughly the same place on each layer.

==Examples==
The following examples jitter the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and jitter.py.

> python jitter.py
This brings up the jitter dialog.

> python jitter.py Screw Holder Bottom.stl
The jitter tool is parsing the file:
Screw Holder Bottom.stl
..
The jitter tool has created the file:
.. Screw Holder Bottom_jitter.gcode

# Lash

This page is in the table of contents.
Lash is a script to partially compensate for the backlash of the tool head.

The lash manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Lash

The lash tool is ported from Erik de Bruijn's 3D-to-5D-Gcode php GPL'd script at:
http://objects.reprap.org/wiki/3D-to-5D-Gcode.php

The default values are from the settings in Erik's 3D-to-5D-Gcode, I believe the settings are used on his Darwin reprap.

==Operation==
The default 'Activate Lash' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===X Backlash===
Default is 0.2 millimeters.

Defines the distance the tool head will be lashed in the X direction.

===Y Backlash===
Default is 0.2 millimeters.

Defines the distance the tool head will be lashed in the Y direction.

==Examples==
The following examples lash the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and lash.py.

> python lash.py
This brings up the lash dialog.

> python lash.py Screw Holder Bottom.stl
The lash tool is parsing the file:
Screw Holder Bottom.stl
..
The lash tool has created the file:
.. Screw Holder Bottom_lash.gcode

# Limit

This page is in the table of contents.

Limit limts the feed rate of the tool head, so that the stepper motors are not driven too fast and skip steps.

==Operation==
The default 'Activate Limit' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Maximum Initial Feed Rate===
Default is one millimeter per second.

Defines the maximum speed of the inital tool head will move.

===Maximum Z Feed Rate===
Default is one millimeter per second.

If your firmware limits the z feed rate, you do not need to set this setting.

Defines the maximum speed that the tool head will move in the z direction.

==Examples==
The following examples limit the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and limit.py.

> python limit.py
This brings up the limit dialog.

> python limit.py Screw Holder Bottom.stl
The limit tool is parsing the file:
Screw Holder Bottom.stl
..
The limit tool has created the file:
.. Screw Holder Bottom_limit.gcode

# Multiply

This page is in the table of contents.
Multiply is a script to multiply the shape into an array of copies arranged in a table.

The multiply manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Multiply

Besides using the multiply tool, another way of printing many copies of the model is to duplicate the model in Art of Illusion, however many times you want, with the appropriate offsets. Then you can either use the Join Objects script in the scripts submenu to create a combined shape or you can export the whole scene as an xml file, which skeinforge can then slice.

==Operation==
The default 'Activate Multiply' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Center===
Default is the origin.

The center of the shape will be moved to the "Center X" and "Center Y" coordinates.

====Center X====
====Center Y====

===Number of Cells===
====Number of Columns====
Default is one.

Defines the number of columns in the array table.

====Number of Rows====
Default is one.

Defines the number of rows in the table.

===Separation over Perimeter Width===
Default is fifteen.

Defines the ratio of separation between the shape copies over the extrusion width.

==Examples==
The following examples multiply the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and multiply.py.

> python multiply.py
This brings up the multiply dialog.

> python multiply.py Screw Holder Bottom.stl
The multiply tool is parsing the file:
Screw Holder Bottom.stl
..
The multiply tool has created the file:
.. Screw Holder Bottom_multiply.gcode

# Oozebane

This page is in the table of contents.
Oozebane is a script to turn off the extruder before the end of a thread and turn it on before the beginning.

The oozebane manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Oozebane

After oozebane turns the extruder on, it slows the feed rate down where the thread starts. Then it speeds it up in steps so in theory the thread will remain at roughly the same thickness from the beginning.

==Operation==
The default 'Activate Oozebane' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===After Startup Distance===
Default is 1.2.

When oozebane reaches the point where the extruder would of turned on, it slows down so that the thread will be thick at that point. Afterwards it speeds the extruder back up to operating speed. The speed up distance is the "After Startup Distance".

===Early Shutdown Distance===
Default is 1.2.

Defines the distance before the end of the thread that the extruder will be turned off. It is the most important oozebane setting. A higher distance means the extruder will turn off sooner and the end of the line will be thinner.

===Early Startup Maximum Distance===
Default is 1.2.

Defines the maximum distance before the thread starts that the extruder will be turned on

===Early Startup Distance Constant===
Default is twenty.

The longer the extruder has been off, the earlier the extruder will turn back on, the ratio is one minus one over e to the power of the distance the extruder has been off over the "Early Startup Distance Constant".

===First Early Startup Distance===
Default is twenty five.

Defines the distance before the first thread starts that the extruder will be turned off. This value should be high because, according to Marius, the extruder takes a second or two to extrude when starting for the first time.

===Minimum Distance for Early Shutdown===
Default is zero.

Defines the minimum distance that the extruder has to be off after the thread end for the early shutdown feature to activate.

===Minimum Distance for Early Startup===
Default is zero.

Defines the minimum distance that the extruder has to be off before the thread begins for the early start up feature to activate.

===Slowdown Startup Steps===
Default is three.

When oozebane turns the extruder off, it slows the feed rate down in steps so in theory the thread will remain at roughly the same thickness until the end. The "Slowdown Startup Steps" setting is the number of steps, the more steps the smaller the size of the step that the feed rate will be decreased and the larger the size of the resulting gcode file.

==Examples==
The following examples oozebane the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and oozebane.py.

> python oozebane.py
This brings up the oozebane dialog.

> python oozebane.py Screw Holder Bottom.stl
The oozebane tool is parsing the file:
Screw Holder Bottom.stl
..
The oozebane tool has created the file:
.. Screw Holder Bottom_oozebane.gcode

# Preface

This page is in the table of contents.
Preface converts the svg slices into gcode extrusion layers, optionally prefaced with some gcode commands.

The preface manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Preface

==Settings==
===Meta===
Default is empty.

The 'Meta' field is to add meta tags or a note to all your files. Whatever is in that field will be added in a meta tagged line to the output.

===Name of Alteration Files===
Preface looks for alteration files in the alterations folder in the .skeinforge folder in the home directory. Preface does not care if the text file names are capitalized, but some file systems do not handle file name cases properly, so to be on the safe side you should give them lower case names. If it doesn't find the file it then looks in the alterations folder in the skeinforge_plugins folder.

====Name of End File====
Default is end.gcode.

If there is a file with the name of the "Name of End File" setting, it will be added to the very end of the gcode.

====Name of Start File====
Default is start.gcode.

If there is a file with the name of the "Name of Start File" setting, it will be added to the very beginning of the gcode.

===Set Positioning to Absolute===
Default is on.

When selected, preface will add the G90 command to set positioning to absolute.

===Set Units to Millimeters===
Default is on.

When selected, preface will add the G21 command to set the units to millimeters.

===Start at Home===
Default is off.

When selected, the G28 go to home gcode will be added at the beginning of the file.

===Turn Extruder Off===
====Turn Extruder Off at Shut Down====
Default is on.

When selected, the M103 turn extruder off gcode will be added at the end of the file.

====Turn Extruder Off at Start Up====
Default is on.

When selected, the M103 turn extruder off gcode will be added at the beginning of the file.

==Examples==
The following examples preface the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and preface.py.

> python preface.py
This brings up the preface dialog.

> python preface.py Screw Holder Bottom.stl
The preface tool is parsing the file:
Screw Holder Bottom.stl
..
The preface tool has created the file:
.. Screw Holder Bottom_preface.gcode

# Raft
This page is in the table of contents.
Raft is a script to create a raft, elevate the nozzle and set the temperature.

The raft manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Raft

Allan Ecker aka The Masked Retriever's has written two quicktips for raft which follow below.
"Skeinforge Quicktip: The Raft, Part 1" at:
http://blog.thingiverse.com/2009/07/14/skeinforge-quicktip-the-raft-part-1/
"Skeinforge Quicktip: The Raft, Part II" at:
http://blog.thingiverse.com/2009/08/04/skeinforge-quicktip-the-raft-part-ii/

Pictures of rafting in action are available from the Metalab blog at:
http://reprap.soup.io/?search=rafting

Raft is based on the Nophead's reusable raft, which has a base layer running one way, and a couple of perpendicular layers above. Each set of layers can be set to a different temperature. There is the option of having the extruder orbit the raft for a while, so the heater barrel has time to reach a different temperature, without ooze accumulating around the nozzle.

If you want to only set the temperature or only create support material or only elevate the nozzle without creating a raft, set the Base Layers and Interface Layers to zero.

The important values for the raft settings are the temperatures of the raft, the first layer and the next layers. These will be different for each material. The default settings for ABS, HDPE, PCL & PLA are extrapolated from Nophead's experiments.

==Operation==
The default 'Activate Raft' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called. The raft script sets the temperature.

==Settings==
===Add Raft, Elevate Nozzle, Orbit===
Default is on.

When selected, the script will also create a raft, elevate the nozzle, orbit and set the altitude of the bottom of the raft.

===Base===
====Base Feed Rate Multiplier====
Default is one.

Defines the base feed rate multiplier. The greater the 'Base Feed Rate Multiplier', the thinner the base, the lower the 'Base Feed Rate Multiplier', the thicker the base.

====Base Flow Rate Multiplier====
Default is one.

Defines the base flow rate multiplier. The greater the 'Base Flow Rate Multiplier', the thicker the base, the lower the 'Base Flow Rate Multiplier', the thinner the base.

====Base Infill Density====
Default is 0.5.

Defines the infill density ratio of the base of the raft.

====Base Layer Height over Layer Thickness====
Default is two.

Defines the ratio of the height & width of the base layer compared to the height and width of the object infill. The feed rate will be slower for raft layers which have thicker extrusions than the object infill.

====Base Layers====
Default is one.

Defines the number of base layers.

====Base Nozzle Lift over Base Layer Thickness====
Default is 0.4.

Defines the amount the nozzle is above the center of the base extrusion divided by the base layer thickness.

===Initial Circling===
Default is off.

When selected, the extruder will initially circle around until it reaches operating temperature.

===Infill Overhang over Extrusion Width===
Default is 0.05.

Defines the ratio of the infill overhang over the the extrusion width of the raft.

===Interface===
====Interface Feed Rate Multiplier====
Default is one.

Defines the interface feed rate multiplier. The greater the 'Interface Feed Rate Multiplier', the thinner the interface, the lower the 'Interface Feed Rate Multiplier', the thicker the interface.

====Interface Flow Rate Multiplier====
Default is one.

Defines the interface flow rate multiplier. The greater the 'Interface Flow Rate Multiplier', the thicker the interface, the lower the 'Interface Flow Rate Multiplier', the thinner the interface.

====Interface Infill Density====
Default is 0.5.

Defines the infill density ratio of the interface of the raft.

====Interface Layer Thickness over Extrusion Height====
Default is one.

Defines the ratio of the height & width of the interface layer compared to the height and width of the object infill. The feed rate will be slower for raft layers which have thicker extrusions than the object infill.

====Interface Layers====
Default is two.

Defines the number of interface layers.

====Interface Nozzle Lift over Interface Layer Thickness====
Default is 0.45.

Defines the amount the nozzle is above the center of the interface extrusion divided by the interface layer thickness.

===Name of Alteration Files===
If support material is generated, raft looks for alteration files in the alterations folder in the .skeinforge folder in the home directory. Raft does not care if the text file names are capitalized, but some file systems do not handle file name cases properly, so to be on the safe side you should give them lower case names. If it doesn't find the file it then looks in the alterations folder in the skeinforge_plugins folder.

====Name of Support End File====
Default is support_end.gcode.

If support material is generated and if there is a file with the name of the "Name of Support End File" setting, it will be added to the end of the support gcode.

====Name of Support Start File====
If support material is generated and if there is a file with the name of the "Name of Support Start File" setting, it will be added to the start of the support gcode.

===Object First Layer Feed Rate Infill Multiplier===
Default is 0.4.

Defines the object first layer infill feed rate multiplier. The greater the 'Object First Layer Feed Rate Infill Multiplier, the thinner the infill, the lower the 'Object First Layer Feed Rate Infill Multiplier', the thicker the infill.

===Object First Layer Feed Rate Perimeter Multiplier===
Default is 0.4.

Defines the object first layer perimeter feed rate multiplier. The greater the 'Object First Layer Feed Rate Perimeter Multiplier, the thinner the perimeter, the lower the 'Object First Layer Feed Rate Perimeter Multiplier', the thicker the perimeter.

====Object First Layer Flow Rate Infill Multiplier====
Default is 0.4.

Defines the object first layer infill flow rate multiplier. The greater the 'Object First Layer Flow Rate Infill Multiplier', the thicker the infill, the lower the 'Object First Layer Flow Rate Infill Multiplier, the thinner the infill.

====Object First Layer Flow Rate Perimeter Multiplier====
Default is 0.4.

Defines the object first layer perimeter flow rate multiplier. The greater the 'Object First Layer Flow Rate Perimeter Multiplier', the thicker the perimeter, the lower the 'Object First Layer Flow Rate Perimeter Multiplier, the thinner the perimeter.

===Operating Nozzle Lift over Layer Thickness===
Default is 0.5.

Defines the amount the nozzle is above the center of the operating extrusion divided by the layer thickness.

===Raft Size===
The raft fills a rectangle whose base size is the rectangle around the bottom layer of the object expanded on each side by the 'Raft Margin' plus the 'Raft Additional Margin over Length (%)' percentage times the length of the side.

====Raft Margin====
Default is three millimeters.

====Raft Additional Margin over Length====
Default is 1 percent.

===Support===
Good articles on support material are at:
http://davedurant.wordpress.com/2010/07/31/skeinforge-support-part-1/
http://davedurant.wordpress.com/2010/07/31/skeinforge-support-part-2/

====Support Cross Hatch====
Default is off.

When selected, the support material will cross hatched. Cross hatching the support makes it stronger and harder to remove, which is why the default is off.

====Support Flow Rate over Operating Flow Rate====
Default is 0.9.

Defines the ratio of the flow rate when the support is extruded over the operating flow rate. With a number less than one, the support flow rate will be smaller so the support will be thinner and easier to remove.

====Support Gap over Perimeter Extrusion Width====
Default is 0.5.

Defines the gap between the support material and the object over the perimeter extrusion width.

====Support Material Choice====
Default is 'None' because the raft takes time to generate.

=====Empty Layers Only=====
When selected, support material will be only on the empty layers. This is useful when making identical objects in a stack.

=====Everywhere=====
When selected, support material will be added wherever there are overhangs, even inside the object. Because support material inside objects is hard or impossible to remove, this option should only be chosen if the object has a cavity that needs support and there is some way to extract the support material.

=====Exterior Only=====
When selected, support material will be added only the exterior of the object. This is the best option for most objects which require support material.

=====None=====
When selected, raft will not add support material.

====Support Minimum Angle====
Default is sixty degrees.

Defines the minimum angle that a surface overhangs before support material is added. This angle is defined from the vertical, so zero is a vertical wall, ten is a wall with a bit of overhang, thirty is the typical safe angle for filament extrusion, sixty is a really high angle for extrusion and ninety is an unsupported horizontal ceiling.

==Examples==
The following examples raft the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and raft.py.

> python raft.py
This brings up the raft dialog.

> python raft.py Screw Holder Bottom.stl
The raft tool is parsing the file:
Screw Holder Bottom.stl
..
The raft tool has created the file:
Screw Holder Bottom_raft.gcode

# Scale

This page is in the table of contents.
Scale scales the carving to compensate for shrinkage after the extrusion has cooled.

It is best to only change the XY Plane Scale, because that does not affect other variables. If you choose to change the Z Axis Scale, that increases the layer thickness so you must increase the feed rate in speed by the same amount and maybe some other variables which depend on layer thickness.

==Operation==
The default 'Activate Scale' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===XY Plane Scale===
Default is 1.01.

Defines the amount the xy plane of the carving will be scaled. The xy coordinates will be scaled, but the perimeterWidth is not changed, so this can be changed without affecting other variables.

===Z Axis Scale===
Default is one.

Defines the amount the z axis of the carving will be scaled. The default is one because changing this changes many variables related to the layer thickness. For example, the feedRate should be multiplied by the Z Axis Scale because the layers would be farther apart..

===SVG Viewer===
Default is webbrowser.

If the 'SVG Viewer' is set to the default 'webbrowser', the scalable vector graphics file will be sent to the default browser to be opened. If the 'SVG Viewer' is set to a program name, the scalable vector graphics file will be sent to that program to be opened.

==Examples==
The following examples scale the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and scale.py.

> python scale.py
This brings up the scale dialog.

> python scale.py Screw Holder Bottom.stl
The scale tool is parsing the file:
Screw Holder Bottom.stl
..
The scale tool has created the file:
.. Screw Holder Bottom_scale.gcode

# Skirt

This page is in the table of contents.
Skirt is a script to give the extruder some extra time to begin extruding properly before beginning the object, and to put a baffle around the model in order to keep the extrusion warm.

It is loosely based on Lenbook's outline plugin:
http://www.thingiverse.com/thing:4918

it is also loosely based on the outline that Nophead sometimes uses:
http://hydraraptor.blogspot.com/2010/01/hot-metal-and-serendipity.html

and also loosely based on the baffles that Nophead made to keep corners warm:
http://hydraraptor.blogspot.com/2010/09/some-corners-like-it-hot.html

If you want only an outline, set 'Layers To' to one. This gives the extruder some extra time to begin extruding properly before beginning your object, and gives you an early verification of where your object will be extruded.

If you also want an insulating skirt around the entire object, set 'Layers To' to a huge number, like 9876554321. This will additionally make an insulating baffle around the object; to prevent moving air from cooling the object, which increases warping, especially in corners.

==Operation==
The default 'Activate Skirt' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Gap over Perimeter Width===
Default is one.

Defines the ratio of the gap between the object and the skirt over the perimeter width. If the ratio is too low, the skirt will connect to the object, if the ratio is too high, the skirt willl not provide much insulation for the object.

====Layers To====
Default is a one.

Defines the number of layers of the skirt. If you want only an outline, set 'Layers To' to one. If you want an insulating skirt around the entire object, set 'Layers To' to a huge number, like 9876554321.

==Examples==
The following examples skirt the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and skirt.py.

> python skirt.py
This brings up the skirt dialog.

> python skirt.py Screw Holder Bottom.stl
The skirt tool is parsing the file:
Screw Holder Bottom.stl
..
The skirt tool has created the file:
.. Screw Holder Bottom_skirt.gcode

# Speed

This page is in the table of contents.
Speed is a script to set the feed rate, and flow rate.

The speed manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Speed

==Operation==
The default 'Activate Speed' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called. The speed script sets the feed rate, and flow rate.

==Settings==
===Add Flow Rate===
Default is on.

When selected, the flow rate will be added to the gcode.

===Bridge===
====Bridge Feed Rate Multiplier====
Default is one.

Defines the ratio of the feed rate on the bridge layers over the feed rate of the typical non bridge layers.

====Bridge Flow Rate Multiplier====
Default is one.

Defines the ratio of the flow rate on the bridge layers over the flow rate of the typical non bridge layers.

===Duty Cyle===
====Duty Cyle at Beginning====
Default is one, which will set the extruder motor to full current.

Defines the duty cycle of the stepper motor pulse width modulation by adding an M113 command toward the beginning of the gcode text. If the hardware has the option of using a potentiometer to set the duty cycle, to select the potentiometer option set 'Duty Cyle at Beginning' to an empty string. To turn off the extruder, set the 'Duty Cyle at Beginning' to zero.

====Duty Cyle at Ending====
Default is zero, which will turn off the extruder motor.

Defines the duty cycle of the stepper motor pulse width modulation by adding an M113 command toward the ending of the gcode text. If the hardware has the option of using a potentiometer to set the duty cycle, to select the potentiometer option set 'Duty Cyle at Beginning' to an empty string. To turn off the extruder, set the 'Duty Cyle at Ending' to zero.

===Feed Rate===
Default is sixteen millimeters per second.

Defines the operating feed rate.

===Flow Rate Setting===
Default is 210.

Defines the operating flow rate.

===Orbital Feed Rate over Operating Feed Rate===
Default is 0.5.

Defines the speed of the orbit compared to the operating extruder speed. If you want the orbit to be very short, set the "Orbital Feed Rate over Operating Feed Rate" setting to a low value like 0.1.

===Perimeter===
To have higher build quality on the outside at the expense of slower build speed, a typical setting for the 'Perimeter Feed Rate over Operating Feed Rate' would be 0.5. To go along with that, if you are using a speed controlled extruder, the 'Perimeter Flow Rate over Operating Flow Rate' should also be 0.5. If you are using Pulse Width Modulation to control the speed, then you'll probably need a slightly higher ratio because there is a minimum voltage 'Flow Rate PWM Setting' required for the extruder motor to turn. The flow rate PWM ratio would be determined by trial and error, with the first trial being:
Perimeter Flow Rate over Operating Flow Rate ~ Perimeter Feed Rate over Operating Feed Rate * ( Flow Rate PWM Setting - Minimum Flow Rate PWM Setting ) + Minimum Flow Rate PWM Setting

====Perimeter Feed Rate over Operating Feed Rate====
Default is one.

Defines the ratio of the feed rate of the perimeter over the feed rate of the infill.

====Perimeter Flow Rate over Operating Feed Rate====
Default is one.

Defines the ratio of the flow rate of the perimeter over the flow rate of the infill.

===Travel Feed Rate===
Default is sixteen millimeters per second.

Defines the feed rate when the extruder is off. The 'Travel Feed Rate' could be set as high as the extruder can be moved, it is not limited by the maximum extrusion rate.

==Examples==
The following examples speed the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and speed.py.

> python speed.py
This brings up the speed dialog.

> python speed.py Screw Holder Bottom.stl
The speed tool is parsing the file:
Screw Holder Bottom.stl
..
The speed tool has created the file:
.. Screw Holder Bottom_speed.gcode

# Splondge

This page is in the table of contents.
Splodge turns the extruder on just before the start of a thread. This is to give the extrusion a bit anchoring at the beginning.

The splodge manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Splodge

==Operation==
The default 'Activate Splodge' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Initial===
====Initial Lift over Extra Thickness====
Default is one.

Defines the amount the extruder will be lifted over the extra thickness of the initial splodge thread. The higher the ratio, the more the extruder will be lifted over the splodge, if the ratio is too low the extruder might plow through the splodge extrusion.

====Initial Splodge Feed Rate====
Default is one millimeter per second.

Defines the feed rate at which the initial extra extrusion will be added. With the default feed rate, the splodge will be added slower so it will be thicker than the regular extrusion.

====Initial Splodge Quantity Length====
Default is thirty millimeters.

Defines the quantity length of extra extrusion at the operating feed rate that will be added to the initial thread. If a splodge quantity length is smaller than 0.1 times the perimeter width, no splodge of that type will be added.

===Operating===
====Operating Lift over Extra Thickness====
Default is one.

Defines the amount the extruder will be lifted over the extra thickness of the operating splodge thread.

====Operating Splodge Feed Rate====
Default is one millimeter per second.

Defines the feed rate at which the next extra extrusions will be added.

====Operating Splodge Quantity Length====
Default is thirty millimeters.

Defines the quantity length of extra extrusion at the operating feed rate that will be added for the next threads.

==Examples==
The following examples splodge the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and splodge.py.

> python splodge.py
This brings up the splodge dialog.

> python splodge.py Screw Holder Bottom.stl
The splodge tool is parsing the file:
Screw Holder Bottom.stl
..
The splodge tool has created the file:
.. Screw Holder Bottom_splodge.gcode

# Stretch

This page is in the table of contents.
Stretch is a script to stretch the threads to partially compensate for filament shrinkage when extruded.

The stretch manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Stretch

All the defaults assume that the thread sequence choice setting in fill is the perimeter being extruded first, then the loops, then the infill. If the thread sequence choice is different, the optimal thread parameters will also be different. In general, if the infill is extruded first, the infill would have to be stretched more so that even after the filament shrinkage, it would still be long enough to connect to the loop or perimeter.

==Operation==
The default 'Activate Stretch' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Loop Stretch Over Perimeter Width===
Default is 0.1.

Defines the ratio of the maximum amount the loop aka inner shell threads will be stretched compared to the perimeter width, in general this value should be the same as the 'Perimeter Outside Stretch Over Perimeter Width' setting.

===Path Stretch Over Perimeter Width===
Default is zero.

Defines the ratio of the maximum amount the threads which are not loops, like the infill threads, will be stretched compared to the perimeter width.

===Perimeter===
====Perimeter Inside Stretch Over Perimeter Width====
Default is 0.32.

Defines the ratio of the maximum amount the inside perimeter thread will be stretched compared to the perimeter width, this is the most important setting in stretch. The higher the value the more it will stretch the perimeter and the wider holes will be. If the value is too small, the holes could be drilled out after fabrication, if the value is too high, the holes would be too wide and the part would have to junked.

====Perimeter Outside Stretch Over Perimeter Width====
Default is 0.1.

Defines the ratio of the maximum amount the outside perimeter thread will be stretched compared to the perimeter width, in general this value should be around a third of the 'Perimeter Inside Stretch Over Perimeter Width' setting.

===Stretch from Distance over Perimeter Width===
Default is two.

In general, stretch will widen holes and push corners out. The algorithm works by checking at each turning point on the extrusion path what the direction of the thread is at a distance of 'Stretch from Distance over Perimeter Width' times the perimeter width, on both sides, and moves the thread in the opposite direction. The magnitude of the stretch increases with the amount that the direction of the two threads is similar and by the '..Stretch Over Perimeter Width' ratio. In practice the filament contraction will be similar but different from the algorithm, so even once the optimal parameters are determined, the stretch script will not be able to eliminate the inaccuracies caused by contraction, but it should reduce them.

==Examples==
The following examples stretch the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and stretch.py.

> python stretch.py
This brings up the stretch dialog.

> python stretch.py Screw Holder Bottom.stl
The stretch tool is parsing the file:
Screw Holder Bottom.stl
..
The stretch tool has created the file:
.. Screw Holder Bottom_stretch.gcode

# Temperature

This page is in the table of contents.
Temperature is a script to set the temperature for the object and raft.

==Operation==
The default 'Activate Temperature' checkbox is on. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Rate===
The default cooling rate and heating rate for the extruder were both been derived from bothacker's graph at:
http://bothacker.com/wp-content/uploads/2009/09/18h5m53s9.29.2009.png

====Cooling Rate====
Default is three degrees Celcius per second.

Defines the cooling rate of the extruder.

====Heating Rate====
Default is ten degrees Celcius per second.

Defines the heating rate of the extruder.

===Temperature===
====Base Temperature====
Default for ABS is two hundred degrees Celcius.

Defines the raft base temperature.

====Interface Temperature====
Default for ABS is two hundred degrees Celcius.

Defines the raft interface temperature.

====Object First Layer Infill Temperature====
Default for ABS is 195 degrees Celcius.

Defines the infill temperature of the first layer of the object.

====Object First Layer Perimeter Temperature====
Default for ABS is two hundred and twenty degrees Celcius.

Defines the perimeter temperature of the first layer of the object.

====Object Next Layers Temperature====
Default for ABS is two hundred and thirty degrees Celcius.

Defines the temperature of the next layers of the object.

====Support Layers Temperature====
Default for ABS is two hundred degrees Celcius.

Defines the support layers temperature.

====Supported Layers Temperature====
Default for ABS is two hundred and thirty degrees Celcius.

Defines the temperature of the supported layers of the object, those layers which are right above a support layer.

==Examples==
The following examples add temperature information to the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and temperature.py.

> python temperature.py
This brings up the temperature dialog.

> python temperature.py Screw Holder Bottom.stl
The temperature tool is parsing the file:
Screw Holder Bottom.stl
..
The temperature tool has created the file:
.. Screw Holder Bottom_temperature.gcode

# Tower

This page is in the table of contents.
Tower commands the fabricator to extrude a disconnected region for a few layers, then go to another disconnected region and extrude there. Its purpose is to reduce the number of stringers between a shape and reduce extruder travel.

The tower manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Tower

==Operation==
The default 'Activate Tower' checkbox is off. The default is off because tower could result in the extruder colliding with an already extruded part of the shape and because extruding in one region for more than one layer could result in the shape melting. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Maximum Tower Height===
Default is five.

Defines the maximum number of layers that the extruder will extrude in one region before going to another. This is the most important value for tower.

===Extruder Possible Collision Cone Angle===
Default is sixty degrees.

Tower works by looking for islands in each layer and if it finds another island in the layer above, it goes to the next layer above instead of going across to other regions on the original layer. It checks for collision with shapes already extruded within a cone from the nozzle tip. The 'Extruder Possible Collision Cone Angle' setting is the angle of that cone. Realistic values for the cone angle range between zero and ninety. The higher the angle, the less likely a collision with the rest of the shape is, generally the extruder will stay in the region for only a few layers before a collision is detected with the wide cone.

===Tower Start Layer===
Default is one.

Defines the layer index which the script starts extruding towers, after the last raft layer which does not have support material. It is best to not tower at least the first layer because the temperature of the first layer is sometimes different than that of the other layers.

==Examples==
The following examples tower the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and tower.py.

> python tower.py
This brings up the tower dialog.

> python tower.py Screw Holder Bottom.stl
The tower tool is parsing the file:
Screw Holder Bottom.stl
..
The tower tool has created the file:
.. Screw Holder Bottom_tower.gcode

# Unpause

This page is in the table of contents.
The unpause script is based on the Shane Hathaway's patch to speed up a line segment to compensate for the delay of the microprocessor. The description is at:
http://shane.willowrise.com/archives/delay-compensation-in-firmware/

The unpause manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Unpause

==Operation==
The default 'Activate Unpause' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Delay===
Default is 28 milliseconds, which Shane found for the Arduino.

Defines the delay on the microprocessor that will be at least partially compensated for.

===Maximum Speed===
Default is 1.3.

Defines the maximum amount that the feed rate will be sped up to, compared to the original feed rate.

==Examples==
The following examples unpause the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and unpause.py.

> python unpause.py
This brings up the unpause dialog.

> python unpause.py Screw Holder Bottom.stl
The unpause tool is parsing the file:
Screw Holder Bottom.stl
..
The unpause tool has created the file:
.. Screw Holder Bottom_unpause.gcode

# Widen

This page is in the table of contents.
Widen will widen the outside perimeters away from the inside perimeters, so that the outsides will be at least two perimeter widths away from the insides and therefore the outside filaments will not overlap the inside filaments.

For example, if a mug has a very thin wall, widen would widen the outside of the mug so that the wall of the mug would be two perimeter widths wide, and the outside wall filament would not overlap the inside filament.

For another example, if the outside of the object runs right next to a hole, widen would widen the wall around the hole so that the wall would bulge out around the hole, and the outside filament would not overlap the hole filament.

The widen manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Widen

==Operation==
The default 'Activate Widen' checkbox is off. When it is on, widen will work, when it is off, widen will not be called.

==Examples==
The following examples widen the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and widen.py.

> python widen.py
This brings up the widen dialog.

> python widen.py Screw Holder Bottom.stl
The widen tool is parsing the file:
Screw Holder Bottom.stl
..
The widen tool has created the file:
.. Screw Holder Bottom_widen.gcode

# Wipe

This page is in the table of contents.
At the beginning of a layer, depending on the settings, wipe will move the nozzle with the extruder off to the arrival point, then to the wipe point, then to the departure point, then back to the layer.

The wipe path is machine specific, so you'll probably have to change all the default locations.

The wipe manual page is at:
http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Wipe

==Operation==
The default 'Activate Wipe' checkbox is off. When it is on, the functions described below will work, when it is off, the functions will not be called.

==Settings==
===Location Arrival===
====Location Arrival X====
Default is minus seventy millimeters.

Defines the x coordinate of the arrival location.

====Location Arrival Y====
Default is minus fifty millimeters.

Defines the y coordinate of the arrival location.

====Location Arrival Z====
Default is fifty millimeters.

Defines the z coordinate of the arrival location.

===Location Departure===
====Location Departure X====
Default is minus seventy millimeters.

Defines the x coordinate of the departure location.

====Location Departure Y====
Default is minus forty millimeters.

Defines the y coordinate of the departure location.

====Location Departure Z====
Default is fifty millimeters.

Defines the z coordinate of the departure location.

===Location Wipe===
====Location Wipe X====
Default is minus seventy millimeters.

Defines the x coordinate of the wipe location.

====Location Wipe Y====
Default is minus seventy millimeters.

Defines the y coordinate of the wipe location.

====Location Wipe Z====
Default is fifty millimeters.

Defines the z coordinate of the wipe location.

===Wipe Period===
Default is three.

Defines the number of layers between wipes. Wipe will always wipe just before layer zero, afterwards it will wipe every "Wipe Period" layers. With the default of three, wipe will wipe just before layer zero, layer three, layer six and so on.

==Examples==
The following examples wipe the file Screw Holder Bottom.stl. The examples are run in a terminal in the folder which contains Screw Holder Bottom.stl and wipe.py.

> python wipe.py
This brings up the wipe dialog.

> python wipe.py Screw Holder Bottom.stl
The wipe tool is parsing the file:
Screw Holder Bottom.stl
..
The wipe tool has created the file:
.. Screw Holder Bottom_wipe.gcode